## Slide 1: Establishing linkages between farm nitrogen surplus and nitrogen concentrations in surface water Csilla Farkas, Moritz Shore, Dominika Krzeminska, Mojtaba Shafiei
Nitrate pollution of drinking water sources /reservoirs
Overall goal: to estimate the health effects and unit prices of drinking nitrate polluted water
Specific goal:
to evaluate the impact of agriculture on nitrate concentration of surface water Pilot site in Czech Republic: Želivka catchment

## Slide 2
Why focusing on agriculture?
Various nitrogen sources
Atmospheric deposition
  (problem at larger scales, other WPs)

## Slide 3
Why focusing on agriculture?
Various nitrogen sources
Atmospheric deposition
  (problem at larger scales, other WPs)
Point sources
  (industry, wastewater treatment plants)

## Slide 4
Why focusing on agriculture?
Various nitrogen sources
Atmospheric deposition
  (problem at larger scales, other WPs)
Point sources
  (industry, wastewater treatment plants)
Diffuse sources
  (manure, mineral fertilizers …. )

## Slide 5
Diffuse nitrogen pollution
” Along with gradually controlled point source discharges, diffuse nitrogen pollution has become an important cause of eutrophication” and water pollution. (Wang et al., Journal of Hydrology, 585:124833)
Atmospheric deposition (commonly cannot be handled locally)
Point sources (sources, allocation, pathways and measures are commonly known)
Diffuse pollution
  Identification of sources
  Determining the main pathways
  Developing retention / removal methods

## Slide 6
Diffuse nitrogen pollution
” Along with gradually controlled point source discharges, diffuse nitrogen pollution has become an important cause of eutrophication” and water pollution. (Wang et al., Journal of Hydrology, 585:124833)
Atmospheric deposition (commonly cannot be handled locally)
Point sources (sources, allocation, pathways and measures are commonly known)
Diffuse pollution
  Identification of sources
  Determining the main pathways
  Developing retention / removal methods
Region- and site specific
Depend on several natural and antrophogenic factors
Require complex assessment

## Slide 7
Impact of agriculture on surface water quality
WE KNOW MUCH
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change

## Slide 8
Impact of agriculture on surface water quality
WE KNOW MUCH
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change
BUT NOT ENOUGH
  Our knowledge is region-, crop-, soil etc. specific
  Can not be extrapolated to so far unknown conditions

## Slide 9
Impact of agriculture on surface water quality
WE KNOW MUCH
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change
BUT NOT ENOUGH
  Our knowledge is region-, crop-, soil etc. specific
  Can not be extrapolated to so far unknown conditions
  Soil- and site specific

## Slide 10
Impact of agriculture on surface water quality
WE KNOW MUCH
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change
BUT NOT ENOUGH
  Our knowledge is region-, crop-, soil etc. specific
  Can not be extrapolated for so far unkown conditions
  Soil-, machinery-, and site specific
  Crop-, soil- and site-specific

## Slide 11
Impact of agriculture on surface water quality
WE KNOW MUCH
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change
BUT NOT ENOUGH
  Our knowledge is region-, crop-, soil etc. specific
  Can not be extrapolated for so far unkown conditions
  Soil- and site specific
  Crop-, soil- and site-specific
  Strongly depend on the type, on local conditions

## Slide 12
Impact of agriculture on surface water quality
WE KNOW MUCH
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change
BUT NOT ENOUGH
  Our knowledge is region-, crop-, soil etc. specific
  Can not be extrapolated for so far unkown conditions
  Soil- and site specific
  Crop-, soil- and site-specific
  Strongly depends on the local conditions
  Cannot be interpreted for future climate conditions

## Slide 13
Some examples
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses
Sources: NICRA, FreePic,

## Slide 14
Some examples
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses
Fucik et al., 2008.
Relationship, developed for the Kopaninsky stream, which is the sub-catchment of Želivka River Basin
It was found that every 10% ploughed land ratio decline within a catchment can cause a drop of surface water nitrate concentration, expressed as C90 value, on average by 6.38 mg/l

## Slide 15
Some examples
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses
Land use change: from arable to grassland
www.frontiersin.org/articles/10.3389/fsufs.2021.706142/full

## Slide 16
Some examples
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses
Land use change: from arable to grassland
New, climate adaptive crops or crop genotypes
mitigate drought
Increases water use efficiency
Increases nutrient use efficiency

## Slide 17
Goal: To understand the naturally observed phenomena and be able to predict them
We do use models for
  developing scientific understanding of complex systems
  spatio-temporal extension of the knowledge gained (data from experiment/monitoring relationships can not be extrapolated in space/time)
  testing the reaction of the system to changing/unobservable conditions
  optimisation, planning and decision-making
Why do we need process-based models?

## Slide 18
Integrate the existing data and knowledge
Incorporate physically based description of various processes
Capable to describe complex systems and relationships
Can be used for
Improving our knowledge about the systems and processes in focus as well as our process-understanding
Extrapolating our knowledge for conditions that we have not experienced before
Optimising various solutions
Tools for establishing linkages between farm nitrogen surplus and nitrogen concentrations in surface water
BUT!!! Should be used following the principles of „good modelling practice”
Process-based environmental models

## Slide 19: Hydro-geochemical models in their respective spatio-temporal scale

## Slide 20: Advantages of using SWAT+ in MARCHES – WHY?
Capable to simulate the processes in focus
Accounts for connectivity
Free software
Widely used and tested
Excellent support team and support group
Spatial aspects of representing a catchment
Implementation of structural measures
Agriculture-oriented (field management schemes, in-field measures)

## Slide 21: Particularities of SWAT+ / disadvantages
Extremely robust model
Extremely data demanding model
Data scarcity problems
Time consuming to set it up and calibrate
Bugs found all the time, newer versions come out
Different version, not easy to find support
Relatively new model (developed from SWAT2012) – documentation is not yet complete

## Slide 22: Modelling workflow
Model setup and parameterisation
  Available data from the study catchment(s) and reach(es)
  Literature review
  Expert assumptions (qualitative information)
Verification
Soft calibration
  Hard calibration (minimizing the difference between measured and modelled discharge and nitrate values)
  Validation
  Scenario analyses (evaluating the effects of NBSs on water quality under present and future conditions)
    Management scenarios
    Implementation of measures
    Climate change scenarios

## Slide 23
Source: K. Bieger et al.

## Slide 24
Source: K. Bieger et al.

## Slide 25: SWAT+ land hydrological processes
Source: K. Bieger et al.

## Slide 26
Forest
Urban
Cropland
Pasture
Oxic Groundwater (near groundwater bodies)
Suboxic Groundwater NO3- N2
Unsaturated
Surface runoff
Sub-surface runoff
Links within the system to be modelled
Modified after Lee at al., 2020;https://doi.org/10.1016/j.envres.2020.109313
Dry deposition
NH4

## Slide 27
Dry deposition
Forest
Urban
Cropland
Pasture
Oxic Groundwater (near groundwater bodies)
Suboxic Groundwater NO3- N2
Unsaturated
Surface runoff
Sub-surface runoff
Links within the system to be modelled
Modified after Lee at al., 2020;https://doi.org/10.1016/j.envres.2020.109313

## Slide 28
SWAT+ data requirement
Digital Elevation Model
Soil data
Land use data
Watershed information
  Catchment boundaries
  Stream network
  Ponds, lakes etc.
Meteorological data
Crop data
Management data
Data on point sources
Reference data for model calibration

## Slide 29
Data-model fusion – an advanced approach for studying complex systems
Model developers
„Modeller”
input data, parameters
reference data
expert estimates
expert evaluation
Modelling is TEAM work

## Slide 30: Local expert knowledge needed for successful soft- and hard calibration
Water balance elements in general (what is realistic)
  Baseflow index in various sub-catchments
  Ratio between surface and subsurface runoff
  Water yield ratio
  Contribution of tile drains

## Slide 31: Local expert knowledge needed for successful soft- and hard calibration
Water balance elements in general (what is realistic)
  Baseflow index in various sub-catchments
  Ratio between surface and subsurface runoff
  Transpiration
  Water yield ratio
  Contribution of tile drains

## Slide 32: Local expert knowledge needed for successful soft- and hard calibration
Water balance elements in general (what is realistic)
  Baseflow index in various sub-catchments
  Ratio between surface and subsurface runoff
  Transpiration
  Water yield ratio
  Contribution of tile drains

## Slide 33: Local expert knowledge needed for successful soft- and hard calibration
Soil and crop management practices since 2013 (information from EUROHARP project)
  Crop rotation
  Tillage systems
  Fertilization practices
  Soil conservation practices

## Slide 34
website of the CHMI https://www.chmi.cz/files/portal/docs/meteo/ok/open_data/Podminky_uziti_udaju.pdf .
information for flow data (average daily flows)
They are publicly available through the ISVS Voda application at: https://isvs.chmi.cz
Surface water quality data
https://isvs.chmi.cz/ords/f?p=11000:HOME:106553409268125:::::
"Water quality in the profile"
Climatological data of the CHMI
daily, monthly and annual climatological characteristics measured at stations under the administration of the CHMI for the period 1961-2022. The data are available https://www.chmi.cz/historicka-data/pocasi/denni-data/Denni-data-dle-z.-123-1998-Sb
No daily data on nitrate concentration is available if using this information.
? EU-level data vs locally available information
Local expert knowledge needed for successful soft- and hard calibration

## Slide 35
Thank you for the attention!

## Slide 42
Steps and constrains of performing scenario analyses
Mathematical models are the best scientific tools to perform scenario analyses as they incorporate physical laws
Empirical models can be used for interpolation but not extrapolation (prediction for unknown situations), as the empirical relationships are valid for the database they have been developed on
The changes evaluated should be not that big, to ensure that the system will be governed by the same physical laws
Calibration and validation
Careful scenario development
Model calibration
Model validation
Implementation of the scenarios (directly, indirectly, or using expert-based estimates)
Evaluation of the scenario results

## Slide 43: SWAT+ compared to SWAT
SWAT+ recent developments
Distinguishes floodplain and highland areas
Decision tables for soil management
Soft-calibration tool
COCOA (Contiguous object connectivity approach)
Field-level management / calculations (reality)
Advanced model setup tool (SWATBuildR
Advanced management scheduling (FarmR)
Advanced soft calibration tool (DoctoR)
Land use map implementing structural measures
Svatools for solving millions if issues
OPTAIN
EU HORIZION 2020
Coordinated by M. Volk

## Slide 44
COCOA : the Contiguous object connectivity approach
Source: Schürz et al.
input
Land object
Flow accumulation
Flow direction
fluxes