## Slide 1: Task 5.1 Water quality modelling Csilla Farkas, Moritz Shore, Dominika Krzeminska, Mojtaba Shafiei, Robert Barneveld
Task 5.1. Drinking water nitrate exposure and catchment-specific unit prices for case study areas
Objective: To develop and apply a rigorous methodology for estimation of health effects and unit prices from drinking nitrate-polluted water in two case study areas by
Modelling of nitrate concentration of surface waters, using the SWAT+ model (CZ, DK)
Modelling of nitrate concentration of shallow groundwater (DK)

## Slide 2
Task 5.1. Drinking water nitrate exposure and catchment-specific unit prices for case study areas
Objective_2: To develop and apply a rigorous methodology for estimation of health effects and unit prices from drinking nitrate-polluted water in case study areas
Methods (to be discussed)
Modelling of nitrate concentration of surface waters, using SWAT+ (CZ, DK)
Modelling of nitrate concentration of shallow groundwater (DK)
Scenario analyses: efficiency of different measures/actions in reducing the nitrate concentration of the water reservoirs used as drinking water sources
Disaggregation of the projected health costs, backtracking to the costs in €/kg of nitrogen-fertilizer surplus lost to the rootzone, and to €/kg of fertilizer-N added to fields
Tracking the data needs to describe, what would be needed for more detailed analyses
Methodology for estimating health effects of nitrate-polluted drinking water

## Slide 3
Case study locations for drinking water nitrate - GREEN
Jutland, Denmark
Zelivka, Czech Republic
Jutland, Denmark
Drinking water is sourced from groundwater
Oxic groundwater bodies
Coupled, surface hydrological and hydrogeological modelling
Nitrate monitoring of drinking water is continuous
Zelivka, Czech Republic
Drinking water is sourced from surface water
Supplies Prague with drinking water
Nitrate concentration is below the WHO threshold, but above the old limits
Nitrate monitoring of drinking water is continuous
Rural locations, predominantly agricultural areas

## Slide 4
Dry deposition
Forest
Urban
Cropland
Pasture
Oxic Groundwater (near groundwater bodies)
Suboxic Groundwater NO3- N2
Unsaturated
Surface runoff
Sub-surface runoff
Links within the system to be modelled
Modified after Lee at al., 2020;https://doi.org/10.1016/j.envres.2020.109313

## Slide 5: Advantages of using SWAT+ in MARCHES – WHY?
Capable to simulate the processes in focus
Accounts for connectivity
Free software
Widely used and tested
Excellent support team and support group
Spatial aspects of representing a catchment
Implementation of structural measures
Agriculture-oriented (field management schemes, in-field measures)

## Slide 6: Particularities of SWAT+ / disadvantages
Extremely robust model
Extremely data demanding model
Data scarcity problems
Time consuming to set it up and calibrate
Bugs found all the time, newer versions come out
Different version, not easy to find support
Relatively new model (developed from SWAT2012) – documentation is not yet complete

## Slide 7: Modelling workflow
Model setup and parameterisation
  Available data from the study catchment(s) and reach(es)
  Literature review
  Expert assumptions (qualitative information)
Verification – SWATdoctR (https://git.ufz.de/schuerz/swatdoctr) AND SWAT+ Editor and Tools
Soft calibration (adjusting yields, baseflow, catchment-level water balance elements)
  Hard calibration (minimizing the difference between measured and modelled discharge and nitrate values)
  Validation
  Scenario analyses (evaluating the effects of NBSs on water quality under present and future conditions)
    Management scenarios
    Implementation of measures
    Climate change scenarios
    Combined scenarios

## Slide 8
SWAT+ data requirement
Digital Elevation Model
Soil data
Land use data
Watershed information
  Catchment boundaries
  Stream network
  Ponds, lakes etc.
Meteorological data
Crop data
Management data
Data on point sources
Reference data for model calibration

## Slide 9
Želivka watershed
Himmerland watershed
Digital elevation model
Copernicus Digital Elevation Model (DEM)
30 m resolution
Copernicus Digital Elevation Model (DEM)
30 m resolution
https://spacedata.copernicus.eu/collections/copernicus-digital-elevation-model.

## Slide 10
Želivka watershed
Himmerland watershed
Land use
CORINE Land Use data (v. 2018)
100 m resolution, raster
https://land.copernicus.eu/
Code | land use type
1 | Continuous urban fabric
2 | Discontinuous urban fabric
3 | Industrial or commercial units
12 | Non-irrigated arable land
18 | Pastures
19 | Annual crops associated with permanent crops
20 | Complex cultivation patterns
21 | Land principally occupied by agriculture with significant areas of natural vegetation
23 | Broad-leaved forest
24 | Coniferous forest
25 | Mixed forest
27 | Moors and heathland
29 | Transitional woodland-shrub
35 | Inland marshes
41 | Water bodies
CORINE Land Use data (v. 2018)
100 m resolution, raster

## Slide 11
Želivka watershed
Himmerland watershed
Soil map
European Soil Database v2.0 (EUSD)
Soil metadata; shape file
Copernicus Digital Elevation Model (DEM)
30 m resolution
(https://esdac.jrc.ec.europa.eu/content/european-soil-database-v20-vector-and-attribute-data#tabs-0-description=0)

## Slide 12
Želivka watershed
Himmerland watershed
Soil data
Soil class | Information
1 | Medium AWC at both top and sub layer. Also contains peat.
2 | Medium AWC at top layer, low AWC at sublayer.
3 | High AWC at both top and sub layer.
4 | Medium AWC at top layer, high AWC at sublayer.
5 | Medium AWC at top layer, low AWC at sublayer.
Soil class | Information
1 | Medium AWC at both top and sub layer.
2 | High AWC at top layer, medium AWC at sublayer.
3 | High AWC at both top and sub layer.
4 | Medium AWC at top layer, low AWC at sublayer.
No. | Parameter | Code
1 | Soil texture (in terms of clay, silt, and sand content in percentage of soil weight) | Texture
2 | Depth of the soil layer in mm | SOL_Z
3 | The number of layers present in the soil profile. | N-layer
4 | Maximum rooting depth of the soil profile | SOL_ZMX
5 | Bulk density in gm/cm3 | SOL_BD
6 | Saturated hydraulic conductivity in mm/hr | SOL_K
7 | Organic carbon content in percentage of soil weight | SOL_CBN
8 | Rock fragment content in percentage of the total weight of that layer | ROCK
9 | Available water capacity of the soil layer in mm H20/mm soil | SOL_AWC
10 | Moist soil albedo only for the topsoil layer | SOL_ALB
11 | Soil hydrologic group (A, B, C or D) | -
12 | Soil erodibility factor K in (metric ton m2 hr)/(m3 metric ton cm) estimated using the Universal Soil Loss Equation | USLE_K

## Slide 13
Želivka watershed
Himmerland watershed
River network and catchment outlet
EU-Hydro River Network Database
Copernicus Digital Elevation Model (DEM)
30 m resolution
https://land.copernicus.eu/en/products/eu-hydro/eu-hydro-river-network-database

## Slide 14
Želivka watershed
Himmerland watershed
Large lakes and reservoirs
World lake database
3 smaller lakes, not visible on map at this scale
World lake database
https://wldb.ilec.or.jp/

## Slide 15
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
https://ec.europa.eu/eurostat/web/lucas

## Slide 16
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
CORINE land use categories

## Slide 17
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities

## Slide 18
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities

## Slide 19
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas

## Slide 20
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas

## Slide 21
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use cathegories into crop communities
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas

## Slide 23
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas
 | Area (% of AGRL) |  |  |  |  |  |  | 
 | 15 | 15 | 15 | 15 | 10 | 10 | 10 | 10
 | Canola | Barley | Corn | wwht | wwht150 | wwht170 | barl100 | barl105
2015 | RAPE | SBARL | CORN | WCER | WCER | WCER | SBARL | SBARL
2016 | SBARL | RAPE | SBARL | SBARL | CORN | WCER | WCER | WCER
2017 | SBARL | SBARL | RAPE | SBARL | WCER | CORN | WCER | WCER
2018 | SBARL | SBARL | SBARL | SBARL | SBARL | RAPE | CORN | WCER
2019 | WCER | CORN | SBARL | RAPE | SBARL | SBARL | SBARL | SBARL
2020 | SBARL | SBARL | SBARL | SBARL | WCER | CORN | RAPE | SBARL
2021 | SBARL | SBARL | SBARL | SBARL | SBARL | WCER | CORN | RAPE

## Slide 24
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas

## Slide 25
Želivka watershed
Himmerland watershed
Preliminary model setup information
https://ec.europa.eu/eurostat/web/lucas

## Slide 26
Želivka watershed
Himmerland watershed
Meteorological input data
ECMWF ERA5 Re-analyses data
Produced by the Copernicus Climate Service
Approx. 31 km resolution
12 grid points within the catchment
https://www.ecmwf.int/en/forecasts/dataset/ecmwf-reanalysis-v5.
ECMWF ERA5 Re-analyses data
Produced by the Copernicus Climate Service
Approx. 31 km resolution
16 grid points within the catchment
Maximum air temperature
Minimum air temperature
Daily precipitation sum
Air humidity
Solar radiation
Wind speed
Maximum air temperature
Minimum air temperature
Daily precipitation sum
Air humidity
Solar radiation
Wind speed

## Slide 27
Želivka watershed
Himmerland watershed
Reference data
Data provided by the Czeh Hydrometeorological Institute
11 stations in total; data for different periods
  Daily average flow
  Water quality data (nitrate)
Surface water database of the Danish Ministry of Environment
Accessible via Aarhus University weebsite
6 stations in total
  Daily average flow
  Nitrate concentration data (bi-weekly)

## Slide 28: Modelling workflow
Model setup and parameterisation
  Available data from the study catchment(s) and reach(es)
  Literature review
  Expert assumptions (qualitative information)
Verification
Soft calibration
  Hard calibration (minimizing the difference between measured and modelled discharge and nitrate values)
  Validation
  Scenario analyses (evaluating the effects of NBSs on water quality under present and future conditions)
    Management scenarios
    Implementation of measures
    Climate change scenarios

## Slide 29
Model verification (highlights)
Želivka

## Slide 30
Model verification (highlights)
Želivka

## Slide 31
Model verification (highlights)
Himmerland

## Slide 32
Soft calibration – crop yields and heat units, Zelivka

## Slide 33
Soft calibration (crop development and yield)

## Slide 34
Hard calibration (ongoing)

## Slide 35: Modelling workflow
Model setup and parameterisation
  Available data from the study catchment(s) and reach(es)
  Literature review
  Expert assumptions (qualitative information)
Verification
Soft calibration
  Hard calibration (minimizing the difference between measured and modelled discharge and nitrate values)
  Validation
  Scenario analyses (evaluating the effects of NBSs on water quality under present and future conditions)
    Management scenarios
    Implementation of measures
    Climate change scenarios

## Slide 36
Želivka watershed
Himmerland watershed
Meteorological input data
ECMWF ERA5 Re-analyses data
Produced by the Copernicus Climate Service
Approx. 31 km resolution
12 grid points within the catchment
https://www.ecmwf.int/en/forecasts/dataset/ecmwf-reanalysis-v5.
ECMWF ERA5 Re-analyses data
Produced by the Copernicus Climate Service
Approx. 31 km resolution
16 grid points within the catchment
Maximum air temperature
Minimum air temperature
Daily precipitation sum
Air humidity
Solar radiation
Wind speed
Maximum air temperature
Minimum air temperature
Daily precipitation sum
Air humidity
Solar radiation
Wind speed

## Slide 37
Želivka watershed
Himmerland watershed
Meteorological input data
Station data from the website of the Czech Hydrometeorological Institute
Danish Meteorological Institute (5 km)
MetNordic data from MetNorway (1 km)
Maximum air temperature
Minimum air temperature
Daily precipitation sum
Air humidity
Solar radiation
Wind speed
https://www.chmi.cz/historicka-data/pocasi/denni-data/Denni-data-dle-z.-123-1998-Sb
https://moritzshore.github.io/miljotools/articles/metno_reanal.html

## Slide 38
Hard calibration (ongoing)
Želivka

## Slide 39
Hard calibration (ongoing)
NSE = 0.43
PBIAS = 6.4%
Želivka

## Slide 40
Želivka watershed
Himmerland watershed
Reference data
ECMWF RE-analyses data (first trial)
(https://cds.climate.copernicus.eu/cdsapp#!/dataset/reanalysis-era5-single-levels?tab=form)
Himmerland

## Slide 41
Himmerland

## Slide 42: Conclusions
Our modelling results are as good as good is our data implemented in the model
Local knowledge, information (quantitative and qualitative) is very important
EU-level available data for the „cooking book” is being tested, BUT so far the results show that data from local authorities, experts etc. are essential for successful model calibration
Plans for improving model performance:
  Using DEM available at national scale (1, 5, 10 m resolution instead of 30 m) - HRU number?
  Applying national datasets for land use and soil
  Using the Google Earth Engine output in a more sophisticated way (SWATfarmR)
  BUT! The catchments are large; trade-off of detailness and robustness

## Slide 43
Želivka watershed
Himmerland watershed
Soil map
European Soil Database v2.0 (EUSD)
Copernicus Digital Elevation Model (DEM)
30 m resolution
(https://esdac.jrc.ec.europa.eu/content/european-soil-database-v20-vector-and-attribute-data#tabs-0-description=0)

## Slide 45
Thank you for the attention!

## Slide 46
Diffuse sources of water pollution from agricultural areas
mitigation measures
Reduced mineral nitrate fertilization
Shifting from mineral fertilization to manure
Cover crops
Others to be defined e.g.
Tillage systems improving soil structure and increasing the wate retention
Vegetation buffer zones
Sedimentation ponds???
Constructed wetlands
OTHER?
Structural measures
Management measures

## Slide 47
Discussion points
Workflow
Link between hydrological and geohydrological modelling work
Selection of mitigation measures (cost?)
  Do we go for structural measures as well?
  What information is needed from measures? (construction costs; maintenance costs?)
What is needed for exposure-response functions (WP2) ? (monthly average concentration in different pathways and reservoirs? )
What is needed for the economic value of the health effects (WP3) ? (cost of mitigation measures?)
Case-study specific discussions
Model’s data demand
Possible date sources
Model structure complexity
Expert knowledge available
Possible benefit from ongoing projects
Etc.

## Slide 48
WHY SWAT+ - pros and contras
data-, work –and time demanding
BUT
spatial distribution, farm-scale

## Slide 49
SWAP model application for evaluating the effect of measures on runoff and water quality
DEM
Land use
Soil map
Map of the watershed with HRU’s
Step 1. Model calibration / testing
Step 2. Estimating the effect of measures under present climate
Step 3. Estimating the effect of various combinations of measures under future climate conditions
+ maps of potential measures in the landscape (modified land use map)

## Slide 50
Results: „non-point sources accounted for 95% of the total nitrate export. Reduction in fertilizer applications from 170 to 50 kg/ha achieved the 38% reduction in nitrate loads. In terms of targeting, the most efficient load reductions occurred when fertilizer applications were reduced in subbasins nearest the watershed outlet.” (Iowa, Keith and Walter, 2009)
A a targeted mineral fertilizer reduction of 23% from the baseline could decrease nitrate leaching and nitrogen emissions by 24% and 21%, respectively, with limited impact on crop yield. In particular, the main effect was observed in the reduction of nitrates transported via groundwater (BFN: 24% of reduction with respect to baseline) followed by nitrogen transported via lateral flow (LFN: 14%) and surface runoff (SRN: 13%). (Malagó et al, 2019; Italy)
Quick literature review on SWAT – Nitrate issues

## Slide 51
Data-model fusion – an advanced approach for studying complex systems
Model developers
„Modeller”
input data reference data
expert estimates
expert evaluation
Modelling is
a
TEAM work

## Slide 52
Steps and constrains of performing scenario analyses
Mathematical models are the best scientific tools to perform scenario analyses as they incorporate physical laws
Empirical models can be used for interpolation but not extrapolation (prediction for unknown situations), as the empirical relationships are valid for the database they have been developed on
The changes evaluated should be not that big, to ensure that the system will be governed by the same physical laws
Calibration and validation
Careful scenario development
Model calibration
Model validation
Implementation of the scenarios (directly, indirectly, or using expert-based estimates)
Evaluation of the scenario results

## Slide 53: SWAT+ compared to SWAT
SWAT+ recent developments
Distinguishes floodplain and highland areas
Decision tables for soil management
Soft-calibration tool
COCOA (Contiguous object connectivity approach)
Field-level management / calculations (reality)
Advanced model setup tool (SWATBuildR
Advanced management scheduling (FarmR)
Advanced soft calibration tool (DoctoR)
Land use map implementing structural measures
Svatools for solving millions if issues
OPTAIN
EU HORIZION 2020
Coordinated by M. Volk

## Slide 54
COCOA : the Contiguous object connectivity approach
Source: Schürz et al.
input
Land object
Flow accumulation
Flow direction
fluxes