## Slide 1: Estimating the nitrogen emissions from agricultural production Csilla Farkas, Moritz Shore, Dominika Krzeminska, Mojtaba Shafiei, Robert Barneveld
Nitrate pollution of drinking water sources /reservoirs
Overall goal: to estimate the health effects and unit prices of drinking nitrate polluted water
Specific goal:
  to evaluate the impact of agriculture on nitrate concentration of surface water (CZ) and groundwater (DK)
  to assess the single and combined effects of mitigation measures on nitrate pollution of drinking water sources

## Slide 2
Why focusing on agriculture?
Various nitrogen sources
Atmospheric deposition
  (problem at larger scales, other WPs)
Point sources
  (industry, wastewater treatment plants)
Diffuse sources
  (manure, mineral fertilizers …. )
” Along with gradually controlled point source discharges, diffuse nitrogen pollution has become an important cause of eutrophication” and water pollution. (Wang et al., Journal of Hydrology, 585:124833)

## Slide 3
Why focusing on agriculture?
Various nitrogen sources
Atmospheric deposition
  (problem at larger scales, other WPs)
Point sources
  (industry, wastewater treatment plants)
Diffuse sources
  Identification of sources
  Determining the main pathways
  Developing retention / removal methods
Region- and site specific
Depend on several natural and antrophogenic factors
Require complex assessment
” Along with gradually controlled point source discharges, diffuse nitrogen pollution has become an important cause of eutrophication” and water pollution. (Wang et al., Journal of Hydrology, 585:124833)

## Slide 4
Impact of agriculture on water quality
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
WE KNOW MUCH
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change

## Slide 5
Some examples of practical experience / knowledge
Sources: NICRA, FreePic
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses

## Slide 6
Some examples of practical experience / knowledge
Sources: NICRA, FreePic
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses
Land use change: from arable to grassland
www.frontiersin.org/articles/10.3389/fsufs.2021.706142/full

## Slide 7
Some examples of practical experience / knowledge – in-field measures
Sources: NICRA, FreePic
Soil tillage: from intensive to extensive systems - increase in water retention and reduction of N losses
Land use change: from arable to grassland
Winter cropping / stubble

## Slide 8
Some examples of practical experience / knowledge – structural measures

## Slide 9
Mitigation measure applicability in the landscape (after Mette Vodder Carstensen, PhD thesis)

## Slide 10
Dry deposition
Forest
Urban
Cropland
Pasture
Oxic Groundwater (near groundwater bodies)
Suboxic Groundwater NO3- N2
Unsaturated
Surface runoff
Sub-surface runoff
Links within the system to be modelled
Modified after Lee at al., 2020;https://doi.org/10.1016/j.envres.2020.109313

## Slide 11
Impact of agriculture on water quality
  Local field-scale experiments
  Data mining and analyses
  Catchment and sub-catchment scale assessments
WE KNOW MUCH
  Impact of soil tillage practices
  Impact of crop management
  Effects of mitigation measures
  Impact of ongoing climate change
  Soil- and site specific
  Crop-, soil- and site-specific
  Strongly depends on the local conditions
  Cannot be interpreted for future climate conditions
BUT NOT ENOUGH
  Our knowledge is region-, crop-, soil etc. specific
  Limited knowledge on the effects of mitigation measures on groundwater nitrate input / concentration
  Can not be extrapolated for so far unknown conditions

## Slide 12
Integrate the existing data, expertise and knowledge
Incorporate physically based description of various processes
Capable to describe complex systems and relationships
Can be used for
Improving our knowledge about the systems and processes in focus and process-understanding
Spatio-temporal extension of knowledge gained
Extrapolating our knowledge for conditions that we have not experienced before
Optimising various solutions for planning and decision-making
Tools for establishing linkages between farm nitrogen inputs and nitrogen concentrations in subsurface water
BUT!!! Should be used following the principles of „good modelling practice”
Process-based environmental models

## Slide 13: Hydro-geochemical models in their respective spatio-temporal scale

## Slide 14: Advantages of using SWAT+ in MARCHES – WHY?
Capable to simulate the processes in focus
Accounts for connectivity
Free software
Widely used and tested
Good support team and support group
Spatial aspects of representing a catchment
Implementation of structural measures
Agriculture-oriented (field management schemes, in-field measures)

## Slide 15: Particularities of SWAT+ / disadvantages
Extremely robust model
Extremely data demanding model
Data scarcity problems
Time consuming to set it up and calibrate
Bugs found all the time, newer versions come out
Different version, not easy to find support
Relatively new model (developed from SWAT2012) – documentation is not yet complete

## Slide 16: Modelling workflow
Model setup and parameterisation
  Available data from the study catchment(s) and reach(es)
  Literature review
  Expert assumptions (qualitative information)
Verification
Soft calibration – verifying the modelling results against expert knowledge, experience
  Hard calibration (minimizing the difference between measured and modelled discharge and nitrate values)
  Validation
  Scenario analyses (evaluating the effects of NBSs on water quality under present and future conditions)
    Management scenarios
    Implementation of measures
    Climate change scenarios

## Slide 17
Information about typical crop rotation and crop yields
Detailed information is available, but extremely time consuming to implement in the SWAT+ model
Characteristic crop- and soil management information
Type and timing of tillage; fertilization amount and timing; winter crops, cover crops, stubble ..
Mitigation measures applied and their effects on water and N fluxes and crop yield
Used for model setup (refining, adjusting the current setup)
Would be important to use for evaluating the results of soft-calibration
Would be important to use for evaluating the first results on the effects of measures
Local expert knowledge useful for successful soft- and hard calibration

## Slide 18
Data-model fusion – an advanced approach for studying complex systems
Model developers
„Modeller”
input data, parameters
reference data
expert estimates
expert evaluation
Modelling is TEAM work

## Slide 19
Stakeholders involvement from modelling prespective
Spring 2024
  Introduce the modelling concept
  Introduce the data implemented in the SWAT+ model
  Show the steps where expert / stakeholder knowledge is highly welcome
Summer 2025
  Joint evaluation of the model soft-calibration results
  Evaluation of the calibration / validation results
  Evaluation of the first results on the effects of mitigation measures
Undefined in 2026
  Presenting and discussing the modelling results (strengths, uncertainty etc.)
  Presenting and discussing the results on mitigation measures
  Discussing the opportunities of reducing nitrate leaching to groundwater systems

## Slide 20
SWAT+ data requirement
Digital Elevation Model
Soil data
Land use data
Watershed information
  Catchment boundaries
  Stream network
  Ponds, lakes etc.
Meteorological data
Crop data
Management data
Data on point sources
Reference data for model calibration

## Slide 21
Digital elevation model
Copernicus Digital Elevation Model (DEM)
30 m resolution
https://spacedata.copernicus.eu/collections/copernicus-digital-elevation-model.
CORINE Land Use data (v. 2018)
100 m resolution, raster
Code | land use type
1 | Continuous urban fabric
2 | Discontinuous urban fabric
3 | Industrial or commercial units
12 | Non-irrigated arable land
18 | Pastures
19 | Annual crops associated with permanent crops
20 | Complex cultivation patterns
21 | Land principally occupied by agriculture with significant areas of natural vegetation
23 | Broad-leaved forest
24 | Coniferous forest
25 | Mixed forest
27 | Moors and heathland
29 | Transitional woodland-shrub
35 | Inland marshes
41 | Water bodies
Land use

## Slide 22
Soil map
European Soil Database v2.0 (EUSD)
Soil metadata; shape file
(https://esdac.jrc.ec.europa.eu/content/european-soil-database-v20-vector-and-attribute-data#tabs-0-description=0)
Soil class | Information
1 | Medium AWC at both top and sub layer. Also contains peat.
2 | Medium AWC at top layer, low AWC at sublayer.
3 | High AWC at both top and sub layer.
4 | Medium AWC at top layer, high AWC at sublayer.
5 | Medium AWC at top layer, low AWC at sublayer.
No. | Parameter | Code
1 | Soil texture (in terms of clay, silt, and sand content in percentage of soil weight) | Texture
2 | Depth of the soil layer in mm | SOL_Z
3 | The number of layers present in the soil profile. | N-layer
4 | Maximum rooting depth of the soil profile | SOL_ZMX
5 | Bulk density in gm/cm3 | SOL_BD
6 | Saturated hydraulic conductivity in mm/hr | SOL_K
7 | Organic carbon content in percentage of soil weight | SOL_CBN
8 | Rock fragment content in percentage of the total weight of that layer | ROCK
9 | Available water capacity of the soil layer in mm H20/mm soil | SOL_AWC
10 | Moist soil albedo only for the topsoil layer | SOL_ALB
11 | Soil hydrologic group (A, B, C or D) | -
12 | Soil erodibility factor K in (metric ton m2 hr)/(m3 metric ton cm) estimated using the Universal Soil Loss Equation | USLE_K
Soil data

## Slide 23
Crop rotation and management
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas

## Slide 24
Želivka watershed
Himmerland watershed
Crop rotation and management
EUROHARP project deliverable
Splitting the AGRL and AGRR CORINE land use categories into crop communities
CORINE land use categories

## Slide 25
Crop rotation and management
Google Earth Engine platform
Uses the EU LUCAS database based on Sentinel data
https://zenodo.org/records/6669644
https://ec.europa.eu/eurostat/web/lucas
 | Area (% of AGRL) |  |  |  |  |  |  | 
 | 15 | 15 | 15 | 15 | 10 | 10 | 10 | 10
 | Canola | Barley | Corn | wwht | wwht150 | wwht170 | barl100 | barl105
2015 | RAPE | SBARL | CORN | WCER | WCER | WCER | SBARL | SBARL
2016 | SBARL | RAPE | SBARL | SBARL | CORN | WCER | WCER | WCER
2017 | SBARL | SBARL | RAPE | SBARL | WCER | CORN | WCER | WCER
2018 | SBARL | SBARL | SBARL | SBARL | SBARL | RAPE | CORN | WCER
2019 | WCER | CORN | SBARL | RAPE | SBARL | SBARL | SBARL | SBARL
2020 | SBARL | SBARL | SBARL | SBARL | WCER | CORN | RAPE | SBARL
2021 | SBARL | SBARL | SBARL | SBARL | SBARL | WCER | CORN | RAPE

## Slide 27
Meteorological input data
ECMWF ERA5 Re-analyses data
Produced by the Copernicus Climate Service
Approx. 31 km resolution
16 grid points within the catchment
https://www.ecmwf.int/en/forecasts/dataset/ecmwf-reanalysis-v5.
Maximum air temperature
Minimum air temperature
Daily precipitation sum
Air humidity
Solar radiation
Wind speed
https://moritzshore.github.io/miljotools/articles/metno_reanal.html
Danish Meteorological Institute (5 km)
MetNordic data from MetNorway (1 km)

## Slide 28
Himmerland watershed
Reference data
Surface water database of the Danish Ministry of Environment
Accessible via Aarhus University weebsite
6 stations in total
  Daily average flow
  Nitrate concentration data (bi-weekly)

## Slide 29: Modelling workflow
Model setup and parameterisation
  Available data from the study catchment(s) and reach(es)
  Literature review
  Expert assumptions (qualitative information)
Verification
Soft calibration
  Hard calibration (minimizing the difference between measured and modelled discharge and nitrate values)
  Validation
  Scenario analyses (evaluating the effects of NBSs on water quality under present and future conditions)
    Management scenarios
    Implementation of measures
    Climate change scenarios

## Slide 30
Model verification (highlights)
Himmerland

## Slide 31
Želivka watershed
Himmerland watershed
Reference data
ECMWF RE-analyses data (first trial)
(https://cds.climate.copernicus.eu/cdsapp#!/dataset/reanalysis-era5-single-levels?tab=form)
Himmerland

## Slide 32
Himmerland

## Slide 33: Conclusions
Our modelling results are as good as good is our data implemented in the model
Local knowledge, information (quantitative and qualitative) is very important
EU-level available data for the „cooking book” is being tested, BUT so far the results show that data from local authorities, experts etc. are essential for successful model calibration
Plans for improving model performance:
  Using DEM available at national scale (1, 5, 10 m resolution instead of 30 m) - HRU number?
  Applying national datasets for land use and soil
  Using the Google Earth Engine output in a more sophisticated way (SWATfarmR)
  BUT! The catchments are large; trade-off of detailness and robustness

## Slide 34
Želivka watershed
Himmerland watershed
Soil map
European Soil Database v2.0 (EUSD)
Copernicus Digital Elevation Model (DEM)
30 m resolution
(https://esdac.jrc.ec.europa.eu/content/european-soil-database-v20-vector-and-attribute-data#tabs-0-description=0)

## Slide 35
Endringer i hydrologiske parameterne i forhold til basisperioden (%) – tiltakseffekter ved maksimalt implementeringsnivå
Q_høy_dag: antall dager med høy (>Qp05) vannføring
Q_lav_dag: antall dager med lav (< Qp90) vannføring
Q_max_min: forskjell mellom maks og min Q

## Slide 36
Endringer i jordvanninnhold i forhold til basisperioden (%) – tiltakseffekter ved maksimalt implementeringsnivå

## Slide 37
Endringer i tap av jordpartikkel og næringsstoffer i forhold til basisperioden (%) – tiltakseffekter ved maksimalt implementeringsnivå

## Slide 38
Demonstrasjon av usikkerhet i modelleringsresultater
Kilder av usikkerhet:
Usikkerhet i inngangsdata
Tidsmessige endringer i parametere (f.eks. jordegenskaper etc.)
Romlig variabilitet av parametere
Forenklinger i modellstruktur/ligninger
Forutsetninger som ble gjort under oppsett av modellen
Usikkerhet i referansedata

## Slide 39
Endringer i de hidrologiske patameterne i forhold til basisperioden (%)
Q_høy_dag: antall dager med høy vannføring
Q_lav_dag: antall dager med lav vannføring
Q_maxmin: forskjell mellom maks og min Q
JV_mai: jordvanninnhold i mai

## Slide 40
Endringer i tap av jordpartikkel og næringsstoffer i forhold til basisperioden (%)

## Slide 41
Thank you for the attention!