## Slide 1
Introduction to hydrological models SWAP theory
Csilla Farkas

## Slide 2
Why do we need process-based models?
Goal: To understand the naturally observed phenomena and be able to predict them
We do use models for
  developing scientific understanding of complex systems
  spatio-temporal extension of the knowledge gained (data from experiment/monitoring relationships can not be extrapolated in space/time)
  testing the reaction of the system to changing/unobservable conditions
  planning and decision-making

## Slide 3
From natural curiosity to data-model fusion
iSock
natural curiosity

## Slide 4
From natural curiosity to data-model fusion
  natural curiosity
  observation
  qualitative information

## Slide 5
From natural curiosity to data-model fusion
iSock
Natural curiosity  observations  information
  Measurements
  data collection
  monitoring
  spatio-temporal databases

## Slide 6
From natural curiosity to data-model fusion
Natural curiosity  observations  information
Measurements  monitoring  databases
  Statistical analyses  empirical models
  Physical laws/relationships 
process-based models
  Models with finer spatio-temporal resolution
Notes: Demand increases + improving computer capacity ; more and more physical relationships and better empirical

## Slide 7
Data-model fusion – an advanced approach for studying complex systems
Model developers
„Modeller”
input data reference data
expert estimates
expert evaluation
Modelling is TEAM work

## Slide 8
Hydrological modelling
Hydrologic models
simplified representation of a hydrological system
aid in understanding, predicting, and managing water resources
study both, flow and quality of water

## Slide 9
Surface
water
Hydrological modelling
Global
water
cycle
Ground-
water
Soil
water
Estuary
Notes: So these are about freshwater modelling .Oceonogy and salt water ecosystems are a separate soil. Water regime of other specific bodies, like wetland, lakes etc.

## Slide 10
Traditional understanding of hydraulic modelling
Soil scientists
Soil water content
Drainage outflow
Hydrologists
Surface runoff
Subsurface runoff
Water quantity and quality at catchment outlet
Notes: Processes, PROPERTIEs. How different processes are expressed etc.

## Slide 11
Hydrological models in the spatio-temporal scale
Hydrogeo-chemical models PERSiST
INCA, HBV SWAT, MIKE
Soil hydrological models (SWAP, HYDRUS, COUP, DrainMod)
aggregation
field
catchment
decades
plot
sub-catchment
region
continent
globe
Spatial scale
m2 km2 102 km2 106 km2
Temporal scale
days
years
mins
hours
Processes in detail
After: Clement et al., 2007
profile
Event-based models
LISEM

## Slide 12
General comparison of different hydrological models

## Slide 13
Processes in focus in different hydrological models

## Slide 14
Model comparision - example

## Slide 15
Modell selection using Benchmark criteria
Source: Farkas et al., 2010.
https://nc.ufz.de/apps/onlyoffice/s/KA9Cr2bbtALGMHr?fileId=117729538

## Slide 16
Task 4.2: Development of modelling protocols
Field-scale model selection
Benchmark criteria in Excel workbook
Completed Benchmark tables (6 partners)
Decision on model selection

## Slide 17
Model selection results – OPTAIN field-scale models
https://nc.ufz.de/apps/onlyoffice/s/KA9Cr2bbtALGMHr?fileId=123941147

## Slide 18
The SWAP soil hydrological model

## Slide 19
The SWAP model domain and processes
Notes: Detailed description of transport of water, solutes and heat within the soil between the layers, de basic element of the soil water balance elements. Layered soil profile. Winter processes, drainage flux. It can also account for fluxes that are very difficult to measure or identify: runon, regional groundwater flux.

## Slide 20
The SWAP - water fluxes between the domains
Notes: Richard’s come out form combining Darcy’s lawe with the continuity equation

## Slide 21
The heart of the model – the Richard’s equation
Darcy’s law
Continuity equation
sink terms
Notes: Highly non-linear equition without general analitical solution. So solves via numerical iteration for each depth and time step.

## Slide 22
Richard’s equation (continued)
q - soil water flux density (cm d-1)
K(h) - hydraulic conductivity (cm d-1)
h - soil water pressure head (cm)
z - vertical coordinate (cm)
θ - volumetric water content (cm3 cm-3)
t - time (d)
q and z are taken positive upward
Sink terms
Sa(h) - extraction rate by plant roots (cm3 cm-3 d-1)
Sd(h) - extraction rate by drain (d-1)
Sm(h) - extraction rate by macro pores (d-1)

## Slide 23
Solving the Richard’s equation
Relationship between Q, h and K
Q - soil water content (cm3 cm-3)
h - soil water pressure head (cm)
K - hydraulic conductivity (cm d-1)
Soil hydraulic functions
Soil water retention curve Q = f(h)
Soil hydraulic conductivity function
  Q = f(K) or h = f(K)
Notes: For solving, we need to know the soil hydrauilc functions

## Slide 24
The SWAP - water fluxes between the domains
Richard’s equation
Manual
Example – Sinja
Notes: Richard’s come out form combining Darcy’s lawe with the continuity equation

## Slide 25
(Feddes, 2007)

## Slide 26
Short introduction to hydrological modelling
Short introduction of the SWAP model structure and theory
Input and reference data requirement
Tools for constructing met input data
Processes, switches and parameters
Reference data quality check
Soft calibration tool
Autocalibration tool
GOAL
to have a finished project for each site
gain knowledge and get tools for further soft- and hard calibration of the SWAP model
The OPTAIN SWAP Workshop

## Slide 27
csilla.farkas@nibio.no
Thank you for your attention!