## Slide 1
Soil parameters and soil input data
Brigitta Szabó and Csilla Farkas

## Slide 2
Soil hydraulic functions – main soil input data
Soil water retention curve; Q = f(h)
Hydraulic conductivity function; K=f(h)
Notes: Needed to ensure continuity;most inportant parameters to fit the soil water section

## Slide 3
  Measurements (lab, in situ)
Measurements are usually done at few – up to 8-10 – data points – NOT enough
We need to fit analytical functions to measured data
Identifying the soil hydraulic functions
  Estimate from other soil properties
= we use pedotransfer functions (PTFs)
We can estimate discrete points and fit an analytical function
We can estimate the parameters of the analytical function directly
Due to the numerical scheme we need continuous functions
The most commonly used analytical description of the two functions is the van Genuchten – Mualem method
Notes: Needed to ensure continuity;most inportant parameters to fit the soil water section

## Slide 4
The van-Genuchten model for soil water retention curves
SWAP manual:
OSAT or Qsat - saturated water content (cm3 cm-3)
ORES or Qres - residual water content (cm3 cm-3)
ALFA or a (cm-1)
NPAR or n (-)
m (-)
empirical shape factors
Notes: Needed to ensure continuity;most inportant parameters to fit the soil water section

## Slide 5
The van Genuchten – Mualem model for the K(h) curve
SWAP manual:
KSATFIT or Ksat- saturated hydraulic conductivity; fitted (cm day-1)
LEXP or l - shape parameter (-)
KSATEXM – measured hydraulic conductivity; fitted (cm day-1)
BDENS – soil bulk density (mg cm-3)
Notes: Needed to ensure continuity;most inportant parameters to fit the soil water section

## Slide 6
Measured and fitted soil water retention curves
Chan et al. 2004
Van-Genuchten model (VG)
Other models
In SWAP you can not define parameters for other models than van-Genuchten – Mualem
Notes: Needed to ensure continuity;most inportant parameters to fit the soil water section

## Slide 7
Soil input data
Parameters of analytical functions
Table format: user-defined data
SWSOPHY
0
1
Notes: Needed to ensure continuity;most inportant parameters to fit the soil water section

## Slide 8
Table format for user-defined data
  h Q K
h – water potential (cm)
Q – soil water content (cm3 cm-3)
K – hydraulic conductivity (cm day-1)
Use small increments
Separate file for each layer

## Slide 9
Table format for user-defined data
  h Q K
h – water potential (cm)
Q – soil water content (cm3 cm-3)
K – hydraulic conductivity (cm day-1)
Use small increments
Separate file for each layer

## Slide 10
  Measurements (lab, in situ)
Fitting analytical functions to measured data
Identifying the soil hydraulic functions
  Estimate from other soil properties
= we use pedotransfer functions (PTFs)
Estimate soil hydraulic functions from properties that are easier to measure
+ you could check https://www.sciencedirect.com/science/article/pii/S0098300421001898
  OPTAIN: Contact Brigi for the WP3 R script
  Outside OPTAIN: contact Brigi and Attila
  BUT…

## Slide 11
  Measurements (lab, in situ)
Fitting analytical functions to measured data
Identifying the soil hydraulic functions
  Estimate from other soil properties
= we use pedotransfer functions (PTFs)
Estimate soil hydraulic functions from properties that are easier to measure
+ you could check https://www.sciencedirect.com/science/article/pii/S0098300421001898
  Outside OPTAIN: contact Brigi and Attila
  BUT…

## Slide 12
  Measurements (lab, in situ)
Fitting analytical functions to measured data
Identifying the soil hydraulic functions
  Estimate from other soil properties
= we use pedotransfer functions (PTFs)
Estimate soil hydraulic functions from properties that are easier to measure
+ you could check https://www.sciencedirect.com/science/article/pii/S0098300421001898
  RETC tool
  ROSETTA neural network

## Slide 13
Using the ROSETTA neural network
Install the HYDRUS-1D model from here: https://www.pc-progress.com/en/Default.aspx?Downloads
Start any of the example projects
Open the table with soil hydraulic properties
Click on Neural Network Prediction
Make your estimation depending on data availability

## Slide 14
Using the ROSETTA neural network

## Slide 15
Using the ROSETTA neural network

## Slide 16
Using the RETC software
Prepare your data in the following format:

## Slide 17
Using the RETC software
Install the RETC from here: https://www.pc-progress.com/en/Default.aspx?retc
Paste your data in the „retention curve data”
Run the program and get your estimates

## Slide 18
csilla.farkas@nibio.no
Thank you for your attention!